## Slide 1
Atmospheric correction of commercial thermal infrared hyperspectral imagery using FLAASH-IR
Steven Adler-Golden, Nevzat Guler and Timothy Perkins
Spectral Sciences, Inc., Burlington, MA 01803
2018 Atmospheric Transmission Models – Modeling in Remote Sensing
4 – 6 June 2018, Boston College

## Slide 2: Outline
Problem Definition
FLAASH-IR Method and Setup
Noise Suppression
Data and Results
  Telops Hyper-Cam LW (see also our previous papers)
  ITRES TASI-600
  SPECIM AisaOWL
Summary and Conclusions

## Slide 3: Problem Definition
Full exploitation of LWIR hyperspectral imagery (HSI) requires atmospheric correction processing
  Retrieval and removal of atmospheric features
  Temperature-emissivity separation (TES) to the extent possible
  SSI has developed FLAASH-IR, a state-of-the-art algorithm based on MODTRAN
We can get good emissivity spectra from sensors like SEBASS and MAKO—what about commercial remote sensors?
  Are the instrument characteristics compatible with FLAASH-IR?
  Is the SNR good enough to yield clean spectra and images?
Mineral Classification Map (from SEBASS): Quartz Alunite Calcite

## Slide 4: Phenomenology Overview
Atmospheric Correction Procedure
  Retrieve atmospheric parameters (water, ozone, temperature)
  Solve for  and TG (temperature-emissivity separation)
At-sensor radiance (at a given wavelength): L = La +  B(TG)atm + (1- )La

## Slide 5: FLAASH-IR Atmospheric Correction
Developed by SSI for automated thermal IR hyperspectral data processing
Constraint is spectrally smooth emissivity
  Radiance error minimization drives the atmosphere and surface temperature solutions
Atmospheric spectral quantities are derived from a 3-D space of variations in air temperature, water vapor and ozone concentration
  Look-up table (LUT) prepared using MODTRAN®
  Atmospheric solution is a polynomial interpolate
Options:
  Spectral polishing (refinement of atmospheric spectra)
  Blackbody illumination component representing clouds, objects on the ground
  Automated spectral calibration refinement

## Slide 6: FLAASH-IR Configuration for Different Sensors
Wavelength range for retrievals
  Typically start at 8.1 µm, end at longest wavelength clean band
Instrument resolution function
  Gaussian for spectrographs and apodized FTIRs
  Sinc function for unapodized FTIRs
  If no FWHMs available, use critical sampling or multiple thereof
Spectral recalibration option
  If wavelengths and FWHMs are not accurately known
  Applies shift and stretch to wavelength scale, scaling to FWHMs
Alternative TES methods
  Normalized Emissivity Method (NEM) and fast linear filter method
  NEM sets maximum emissivity to 0.98; useful for natural materials, dry atmosphere, lower spectral resolution

## Slide 7: Noise Suppression Algorithm
Background noise is prominent in commercial HSI sensors
  Due to cost and size/weight limitations (FPA and cooling system)
Maximum Noise Fraction (MNF) transformation is the foundation of a number of de-noising methods
  Equalizes the noise across wavelengths, transforms to principal component (PC) space
  Noise-dominated “late” PCs are suppressed, then data are reconstructed
We have developed a patent-pending version of MNF denoising based on Bayesian Signal Estimation
  Analytical “shrinkage functions” that shrink small values but preserve large values are applied to the PC eigenimages
  In contrast to PC truncation, this method largely preserves anomalous spectra, while effectively aggregating abundant spectra
Algorithm is applied to the radiance data

## Slide 8: Bayesian Signal Estimation (BSE) and Shrinkage Functions
The BSE formula uses assumed probability distributions for the signal and noise values to estimate the noise-free signal
  The best-estimate signal is obtained by averaging over the continuum of noise models, weighted by Gaussian noise PDF (G) and signal prior PDF (P)
Result: Estimated x given observation y is a ratio of convolutions
x’(y) = (G * (x P(x)) )(y) / (G * P)(y)
The ratio S(y) = x’/y is < 1 and is called the shrinkage function
  We use the expression S(y)=1/ [r exp(-y2)+1] where r is a function of the PC number
  This is an analytical solution for a late-PC PDF consisting of a flat signal distribution (rare and anomalous spectra: large values) plus a delta function distribution (common material spectra: near zero values)

## Slide 9: Outline
Problem Definition
FLAASH-IR Method and Setup
Noise Suppression
Data and Results
  Telops Hyper-Cam LW (see also our previous papers)
  ITRES TASI-600
  SPECIM AisaOWL
Summary and Conclusions

## Slide 10: Telops Hyper-Cam LW
~8-11.5 µm imaging FTIR, Stirling-cooled MCT
Spectral resolution from 0.25-150 cm-1
Georectified mosaics
De-noised
Farmland south of Quebec City
De-noising cleans the spectra and stabilizes the TES
RGB = 8.5, 9.5, 10.5 µm

## Slide 11: ITRES TASI-600
~8-11.5 µm refractive spectrometer, cryogenically cooled MCT
Spectral resolution ~0.13 µm
Georectified mosaics
Cuprite, NV
Absolute emissivities are slightly better with the NEM for this scene, sensor and atmosphere

## Slide 12: Adequacy of TASI Spectral Resolution for Mineral Mapping
TASI
SEBASS
JHU Library
SEBASS
JHU Library

## Slide 13: Emissivity False Color Image Provides a Rough Mineral Map
710 x 570 m, NEM, De-noised
RGB = 8.2, 10.0, 11.5 µm
Quartz
Alunite
Calcite

## Slide 14: Urban TASI Data – Beauport
Google Maps
Radiance
FLAASH-IR Emissivity (no de-noising)
R=11.2µm G=10.4 µm B=9.1µm

## Slide 15: SPECIM AisaOWL
~8-12.3 µm grating spectrometer, Stirling-cooled MCT
Spectral resolution 0.10 µm
Georectified mosaics
South Cornelly, UK stone quarry (de-noised)
Quartz
Blackbody
Calcite?
RGB = 8.5, 10.0, 11.5 µm

## Slide 16: Summary & Conclusions
FLAASH-IR works well with all three commercial sensors
The Hyper-Cam LW has the best SNR and spectral resolution
  Good SNR likely due to the FTIR multiplex advantage
The AisaOWL has the widest spectral range
  Usable response almost 1 µm beyond the other two sensors
All three sensors benefit from noise suppression
All three sensors should be useful for surface classification
These sensors may not have enough SNR and/or spectral range for stressing applications in rare-material and low-concentration gas detection
  Noise suppression probably cannot help here
Acknowledgements: SSI IR&D; Martin Chamberland (Telops), Jason Howse (ITRES), Timo Hyvarinen (SPECIM)